DAYCARE CENTER PRE-INSPECTION CHECKLIST

The following information is designed to help you identify potential fire code violations.  These sections represent the areas where most problems are found.  If you complete this checklist prior to Fire Department personal inspecting your Daycare Center, you will greatly reduce your chances of having any violations.  If you have additional questions, please contact the Licensed Care Facility Inspector at 253.591.5740.

| FIRE SYSTEMS | YES | NO | N/A |
| --- | --- | --- | --- |
| Manual fire alarm system if over 50 children or 5 or more if 2-½ years or younger. (IFC 907.2.6) |  |  |  |
| 2A10BC fire extinguisher within 75’ travel distance of ALL portions of the building, on every floor level and in cooking areas.(IFC 906.3, 906.5) |  |  |  |
| Fire protection systems are maintained and not obstructed or otherwise impaired. (IFC 901.6, 901.7) |  |  |  |
| Smoke detectors are installed in each story in front of doors to stairways and in corridors of all floors occupied by the facility. Detectors are also installed in lounges, recreation areas, and sleeping rooms. (IFC 907.2.6) |  |  |  |
| The fire alarm system is supervised by an approved central, proprietary, or remote station service for daycares licensed for over 50 children or 5 or more if 2 ½ years or younger. (IFC 907.2.6) |  |  |  |
| The fire alarm system and smoke detectors are maintained in an operative condition (IFC 901.6) |  |  |  |
| In facilities not required to have a fire alarm system, single station smoke detectors are placed in each story in front of doors to the stairways and in the corridors of all floors occupied by the facility. Detectors are also installed in lounges, recreation areas and sleeping rooms. (IFC 907.2.10) |  |  |  |
| An automatic sprinkler system is installed in the basement when the basement is larger than 1500 square feet in floor area. (IFC 903) |  |  |  |
| Automatic sprinkler system installed throughout the building when child care center is located above the first story. (IFC 903) |  |  |  |
| Annual service inspection shall be done for all fire alarms, sprinkler systems and extinguishers. (IFC 901.6.2) |  |  |  |

| ELECTRICAL |
| --- |
| Extension cords not used as permanent wiring and visible electrical problems (IFC 605.5) |  |  |  |
| Work space around switchboards and panel boards is clear and unobstructed with a minimum width of 30 inches and a minimum height of 78 inches. (IFC 605.3) |  |  |  |

| COMMERCIAL HOODS |
| --- |
| Commercial hoods will be cleaned and serviced every 6 months. (IFC 904.11.6.4) |  |  |  |
| Annual servicing of extinguishers with tag. (IFC 901.6.1) |  |  |  |
| Class K fire extinguishers shall be installed within 30 feet of commercial cooking. (IFC 906.11.5) |  |  |  |

| EXITS |
| --- |
| Two ways out of all sleeping and napping rooms. One exit may be a window, if sill is not over 44 inches high and opening is minimum 20 in width and 24 inches in height. (IFC 1026.2.1) |  |  |  |
| Basements and second floors not used for day care unless one exit leads directly to exterior. No day care on third floor or above. |  |  |  |
| A minimum of two approved exits are provided where the number of occupants is at least 10. (IFC 1015.1) |  |  |  |
| Exit doors are maintained in an operable condition and shall open in the direction of travel when occupant load is at least 50. (IFC 1008.1) |  |  |  |
| Panic Hardware required when capacity is 50 or more |  |  |  |
| Exit doors are open with a single action or motion without the use of a key or any special knowledge or effort. (IFC 1008.1.8) |  |  |  |
| Exit doors are not locked, chained, bolted, barred, latched, or otherwise rendered unusable. (IFC 1008.1.8) |  |  |  |
| Manually operated dead bolts or surface bolts on exit door not permitted. (IFC 1008.1.8.4) |  |  |  |

| EXIT SIGNS AND ILLUMINATION |
| --- |
| Exit illumination is provided and maintained at all times. (IFC 1011.2, 1011.5.3) |  |  |  |
| The power supply for exit illumination, where the exiting system serves an occupant load of 100 or more, is automatically provided from an emergency system. (IFC 1027.5) |  |  |  |
| Exit signs are provided from each story, room, or area when two or more exits are required. (IFC 1011.1) |  |  |  |
| Directional exit signs are provided where the exit way is not easily identified from any part of the building. (IFC 1011.1) |  |  |  |
| Emergency lighting with battery back up power required. (IFC 1006.1, 1006.3) |  |  |  |
| Address unobstructed and plainly visible from the street |  |  |  |

| STAIRWAYS |
| --- |
| Each floor above and below grade have at least 2 exit stairs or one exit that opens directly to grade level (WAC 170-296-0560) |  |  |  |
| Barriers are provided and maintained to prevent exit traffic ascending or descending a stairway from going beyond the grade level. |  |  |  |

| STORAGE |
| --- |
| Hazardous room not accessible to children and separated by one hour construction. (WAC 170-296-5060) |  |  |  |
| Housekeeping in all areas satisfactory. No buildup of combustibles and proper storage of hazardous material. (IFC 315.5) |  |  |  |
| No obstructions, including storage, are placed in the required width of an exit. (IFC 315.22, 1003.6) |  |  |  |
| There is no storage under stairways, except stairways that are protected on the enclosed side by 1-hour fire resistive construction. (IFC 315.2, 315.2.3) |  |  |  |
| No combustibles stored near heating equipment, boiler rooms, mechanical rooms or electrical rooms. (IFC 315.2.3) |  |  |  |
| Fueling equipment is not stored, operated, or repaired in center. |  |  |  |
| Decorative material is flame resistant. Artwork and teaching material may be attached directly to the walls if they do not exceed 20% of the wall area. (IFC 807.4.4) |  |  |  |

| DISASTER PLANNING |
| --- |
| Fire/Disaster drill documentation (IFC 405) |  |  |  |
| Fire evacuation plan on premises and staff knowledgeable (IFC 404.2) |  |  |  |
| Written Plan for both Fire and Disaster (IFC 404.2) |  |  |  |
| Out of state Contacts (WAC 170-295-7080) |  |  |  |
| First Aid supplies adequate for center (WAC 170-295-5010) |  |  |  |

# Text boxes

# Tacoma Fire Department
Prevention Bureau 253.591.5740
FAX Number 253.594.7943 
3471 S. 35th St. Tacoma, WA 98409